## Slide 1
Shahoshi
Multimodal Edge ML for Women's Safety Wearable
HCI Research Proposal
Group – Shahoshi
Asif Zaman - 25-93713-1
Sabiha Khair Ohi - 25-93714-1
Marmita paul - 25-93603-1
1,500
BDT Target Cost
95%+
Detection Accuracy
6 Wks
Build Timeline

## Slide 2
The Problem
Safety Gap for Women
1. Existing devices require a manual button press
2. Smartphone-dependent apps fail when phones are grabbed or switched off
3. Cloud-based solutions are useless without internet connectivity
4. Retail safety wearables cost 3,000–10,000 BDT unaffordable for most
5. No solution performs passive, automatic threat detection on-device
SafeBand (2018) — Closest Prior Work
✗ Manual trigger
→ Passive ML detection
✗ Accel only
→ Accel + Gyro + HR + Noise + GPS
✗ Smartphone dependent
→ Fully on-device
✗ No ML model
→ TFLite Multimodal Fusion
✗ 1,500–2,000 BDT
→ Target: 1,000–1,500 BDT

## Slide 3
Previous Works — Bangladesh (Local)
Project
Year
Key Method
Sensors
Accuracy / Performance
Limitation
SafeBand
2018
Manual SOS button + threshold accel
Accelerometer
N/A (manual trigger); 18–20 hr battery
No ML
phone needed
BOHNNI / BADHON
2021
GPS tracking + GSM SMS alert
GPS + GSM
N/A (manual trigger)
No anomaly detection

## Slide 4
Previous Works — Global
Project / Paper
Year / Country
Method
Sensors
Accuracy / Metric
Gap vs SheShield
We'RSafe
2017 · India
Mobile app SOS + live location share
GPS (phone)
App-based; no detection metric
No wearable, no ML
FEMME Device
2016 · India
Wearable + mobile app alert
GPS + GSM
Manual trigger only
Phone dependency
Edge IOT Facilitated Multimodal Sensor fusion for Threat Recognition (IEEE)
2025 · Global
Sensor fusion + Cloud supported alerts
Accel + Gyro
93% accuracy (UCI HAR)
Limited modality
Cloud rely
Freezing of Gait (IEEE Biomed.)
2025 · Global
EEG + EMG multi-sensor fusion, edge ARM MCU
EEG + EMG
0.81 sens, 0.88 spec, <100ms
Medical only, not safety
CNN-LSTM HAR (Deep Learning)
2024 · Global
CNN-LSTM on accelerometer data
Accel only
99.3% accuracy (UCI HAR)
Single modality, no edge deploy
CAE + BiLSTM Anomaly
2023 · Global
Unsupervised Conv Autoencoder + BiLSTM + Attention
Multi-sensor time series
State-of-the-art on HAR/HC
Not deployed on-device

## Slide 5
Shahoshi: Proposed Solution
Movement
MPU-6050
Accel + Gyro
Struggle / gait anomaly
Heart Rate
MAX30100
PPG Optical
Panic spike detection
Acoustic
MAX4466 Mic
Environmental audio
Scream / distress detection
Location (optional)
ATGM336H GPS
Spatial anomaly
Unusual stationary position
▼ Two-of-Three Consensus → Multimodal Fusion Engine (TFLite Micro on ESP32) ▼
Local Inferencing
Triggers on-device with no cloud/internet needed
SOS via GSM/BT
Sends SMS alert with location to emergency contacts
<200ms Latency
Real-time response on 240 KB RAM ESP32

## Slide 6
Research Novelties & Contributions
1. Passive Detection
No victim action required. ML automatically flags threat — critical when the victim cannot press a button.
2. Multimodal Fusion Engine
First to combine Accel + Gyro + HR + Noise + GPS for assault detection on edge hardware.
3. Fully On-Device
Triggers and alerts without cloud or smartphone. Works in dead zones, underground, anywhere.
4. Dataset Fusion Strategy
Novel approach: temporal alignment of 5 disparate public datasets as training data for edge ML.
5. Ultra-Low Cost
1,000–1,500 BDT prototype vs. 3,000–10,000 BDT retail. Viable for Bangladesh's market.
6. HCI / TUI Study
Explicit wearability and social acceptability evaluation with women — what SafeBand never did.

## Slide 7
Technical Architecture
ML Stack
1D-CNN —
Temporal feature extraction from sensor windows (150-step)
Bi-LSTM —
Sequential anomaly pattern learning across modalities
Attention —
Weights dangerous sensor combinations higher
Fusion Head —
Binary: threat / no-threat with 2-of-3 consensus vote
Quantized —
~150–200 KB model — fits ESP32's 520 KB RAM
Training Datasets
Movement
UCI HAR + MotionSense
Accel/Gyro, 50 Hz
Heart Rate
WeSAD
Stress-state HR spikes as panic proxy
Acoustic
ESC-50 + UrbanSound8K
Scream vs ambient classes
Location
GeoLife (Microsoft)
Normal vs anomalous GPS patterns
Multimodal
EmoWear (2024)
HR + emotion + IMU, brand new

## Slide 8
Cost Breakdown — Target: 1,000–1,500 BDT/unit
Component
Specification
Cost (BDT)
ESP32-C3 SuperMini
MCU + BLE/WiFi + Edge ML
300
MPU-6050 (IMU)
6-axis Accel + Gyro
200
MAX30100
Heart Rate (PPG Optical)
250
MAX4466 / INMP441
Microphone / Noise Sensor
230
ATGM336H GPS (optional)
Budget GPS (vs NEO-6M at 900 BDT)
350
LiPo Battery 300mAh
Power supply
150
Casing & Misc
3D print + wires
100
TOTAL — 1 Prototypes + R&D Budget:
BDT 1580

## Slide 9
6-Week Sprint Timeline
Week 1–2
Data Fusion & ML Development
▸ Download & temporally align UCI HAR, WeSAD, ESC-50, GeoLife
▸ Build Multimodal Fusion Engine (1D-CNN + Bi-LSTM) [Or any other approach]
▸ Quantize model to INT8 for TFLite Micro (target: <200 KB)
Week 3–4
Hardware Prototyping
▸ Assemble ESP32 + MPU-6050 + MAX30100 + Mic + GPS
▸ Port TFLite model to ESP32 (TFLite Micro API)
▸ Validate on-device inference trigger (2-of-3 consensus)
Week 5–6
Testing, Refinement & Documentation
▸ Testing for trigger accuracy & false-positive rate (<2%)
▸ HCI / wearability study with target users + Baseline comparison
▸ Final report + publication-ready paper draft

## Slide 10
References
[1] Islam, M. et al. (2018). SafeBand: A Wearable Device for the Safety of Women in Bangladesh. IEEE ICECE 2018.
[2] BOHNNI / BADHON Project Report (2021). Jewelry-form GPS+GSM women safety wearable, Bangladesh.
[3] Malekzadeh, M. et al. (2019). MotionSense Dataset. GitHub: mmalekzadeh/motion-sense.
[4] Anguita, D. et al. (2013). UCI Human Activity Recognition Dataset. UCI ML Repository.
[5] Schmidt, P. et al. (2018). WeSAD: A Multimodal Dataset for Wearable Stress and Affect Detection. ICMI 2018.
[6] Piczak, K.J. (2015). ESC: Dataset for Environmental Sound Classification. ACM Multimedia 2015.
[7] Zheng, Y. et al. (2011). GeoLife: Building Social Networks Using Human Location History. Microsoft Research.
[8] Sarkar, A. et al. (2024). Real-Time Anomaly Detection on Wearables using Edge AI. IJERT, Vol. 13, 2024.
[9] Chen, X. et al. (2025). Multi-Modal Flexible Sensors with Edge DL for Freezing of Gait. IEEE J. Biomed. Eng., 2025.
[10] Xu, Z. et al. (2023). Unsupervised Deep Anomaly Detection on Multi-Sensor Time Series. arXiv:2307.XXXXX.
[11] Ahmed, N. et al. (2024). Deep Learning for Wearable Activity Recognition: CNN-LSTM Hybrid. Sensors, 2024.
[12] Shi, J. et al. (2024). EmoWear: Emotion + Activity Multimodal Wearable Dataset. Nature Sci. Data, 2024.
[13] Goldberger, A. et al. (2000). PhysioBank, PhysioToolkit, and PhysioNet. Circulation, 101(23).
[14] We'RSafe App (2017). Mobile-based personal safety application, India.
[15] FEMME Wearable Device (2016). GPS+GSM wearable safety device concept, India.
[16]R. Deepa, A. Packialatha and G. Rajaram, "Edge-IoT Facilitated Multimodal Sensor Fusion for Threat Recognition in Women's Safety Wearables,
* All datasets are publicly available. Papers cited per IEEE/ACM citation style.